## Slide 1: Computer Architecture
Fundamentals of quantitative design and analysis
Daisy Opanga SCT212-0052/2021

## Slide 2: Introduction: The Evolution of Computer Architecture(CA)
Technological advancement during the period (1940s–2000s) has lead to dramatic performance gains culminating to today’s $500 device outperforming a $1M 1985 system.
This is majorly as a result of:
  Technology scaling (Moore’s Law, transistor miniaturization)
  Architectural innovations (RISC, pipelining, caching, ILP)
Some of the architectural milestones achieved during this period include:
1970s–1980s: Microprocessors emerged, enabling mass production and higher growth (~35%/year).
1980s: RISC architectures thrived due to simpler instructions and faster execution.
Intel’s strategy: x86 instructions translated into internal RISC-like micro-ops.
RISC caused legacy systems like VAX to be phased out while ARM grew in the mobile space.
In 1985–2003: Performance growth peaked at 52%/year due to architectural advances causing 25,000× improvement over 1978 systems.
This enabled high-level languages and powerful consumer hardware.

## Slide 3: Introduction: The Evolution of Computer Architecture(CA)
Post 2003 growth slowed to around less than 22%/year. This resulted from limited power and ILP.
Intel ended their fast uniprocessor efforts and shifted their design focus from Instruction-Level Parallelism (ILP) to other types of parallelism, including: Data-Level (DLP), Thread-Level (TLP) and Request-Level (RLP) Parallelism.
This shift required explicit parallel programming to be done by the programmers, a major shift for software development.
Other systemic Impacts included:
  Microprocessors replacing minicomputers, mainframes and even supercomputers.
  New classes of devices emerged, for instance: mobile clients, warehouse-scale computers.
  Software evolves from mainly being programmed in C/C++ to Java, Python and use of newer technology like SaaS and just-in-time compilers.
  Adoption of quantitative design approach employing empirical, simulation-based and measurement-driven methodology. This aims to Balance performance, power, cost and complexity.

## Slide 4: Aspects of Computer Architecture
Computer Architecture includes several aspects that influence system performance and design for instance:
  Instruction Set Architecture (ISA):
    The interface between hardware and software.
    Includes instruction formats, addressing modes, operations, etc.
  Microarchitecture:
    The implementation of the ISA in hardware.
    Determines data-path design, control logic, pipeline stages, etc.
  System Design:
    Covers memory hierarchy, interconnects, I/O systems and more.

## Slide 5: Principles of Computer Design
Key principles that help guide effective hardware development include:
  Design for Performance using Parallelism
    Includes instruction-level parallelism (ILP), pipelining, multicore systems.
  Design for Efficiency
    Utilize hardware resources optimally (area, power, energy).
  Make the Common Case Fast
    Optimize for operations most frequently used by applications.
  Performance via Predictability
    Reduce stalls by prediction (e.g., branch prediction).
  Locality of Reference
    Programs tend to use a relatively small portion of memory at a time.

## Slide 6: Parallelism and Parallel Architectures
Types of Application Parallelism include:
  Data-Level Parallelism (DLP): Apply the same operation across many data items (e.g., vector operations).
  Task-Level Parallelism (TLP): Execute independent tasks simultaneously (e.g., web servers, search queries).
These 2 types can be applied by computer hardware in the following ways:
  Instruction-Level Parallelism (ILP): Modest DLP via pipelining, superscalar, speculative execution.
  Vector Architectures & GPUs: High DLP using SIMD, same instruction over multiple data.
  Thread-Level Parallelism (TLP): Multiple threads working together (shared memory/multicores).
  Request-Level Parallelism (RLP): Decoupled tasks, often used in servers or warehouse-scale computing.

## Slide 7: Classes of Computers: Flynn’s Taxonomy
SISD:
  One instruction stream, one data stream.
  Traditional uniprocessor systems.
  Uses ILP to improve speed.
SIMD:
  One instruction stream, multiple data streams.
  Good for data-parallel tasks (e.g., GPUs, vector units).
MISD:
  Multiple instruction streams, one data stream.
  Mostly theoretical; no practical commercial systems.
MIMD:
  Multiple instructions, multiple data streams.
  Most general and flexible.
  Used in multicore, clusters, and cloud systems.
  Supports both DLP and TLP, but with more complexity.
Modern processors often combine elements of a number of these models hence they are not cast on stone.

## Slide 8: ISA Dimensions
Register Model:
  General-purpose vs. floating-point registers; register-memory (x86) vs. load-store (ARM/MIPS).
Memory Addressing:
  Byte-addressable; alignment requirements vary (ARM/MIPS require aligned accesses).
Addressing Modes:
  MIPS: register, immediate, displacement.
  x86/ARM: plus PC-relative, scaled/indexed, auto-increment/decrement.
Operand Types & Sizes:
  8-, 16-, 32-, 64-bit integers; IEEE-754 single/double; x86 also offers 80-bit FP.
Operation Classes:
  Data transfer, integer ALU, control flow, floating point (MIPS example is RISC-friendly).
Control Flow:
  PC-relative branches/jumps; MIPS tests registers, x86/ARM test condition codes; call/return differences.
Encoding:
  Fixed-length (32-bit ARM/MIPS) simplifies decode; variable-length (x86) reduces program size.

## Slide 9: Trends in Technology
ISAs must be designed to outlast rapid technology shifts (e.g., IBM mainframe ISA in use for around 50 years).
Five Fast-Moving Technologies:
  IC Logic: Transistor counts grow ~40-55%/yr (doubling 18-24 months) per Moore’s Law; die size increase by 1-20%/yr.
  DRAM: Capacity grows 25-40%/yr (doubling every 2-3 yrs), but growth is slowing and may hit a wall.
  Flash: Non-volatile memory grows 50-60%/yr (doubling ~2 yrs); today its ~15-20× cheaper per bit than DRAM.
  Disk: Density growth: 30%/yr pre-1990, 100%/yr mid-90s, ~40%/yr now (doubling ~3 yrs);
  cost per bit ~300–500× cheaper than DRAM.
Networks: Bandwidth and switch/transmission tech continuously improve.
Technology Thresholds: When device density hits a point, new capabilities emerge (e.g., single-chip 32-bit CPUs, on-chip caches, multicore).
Bandwidth vs. Latency: Across CPUs, memory, networks, disks:
  Bandwidth gains (x300-25 000) far outstrip latency gains (x6-80).
  Rule of thumb: bandwidth scales roughly with the square of latency improvement.

## Slide 10: Trends in Technology
Transistor vs. Wire Scaling:
  Transistors: Shrinking feature sizes yield quadratic density increases and roughly linear speedups per generation.
  Wires: As dimensions shrink, resistance x capacitance delays worsen; wire delay has become a primary design constraint alongside power.
Transistor Count:
  Grew exponentially following Moore’s Law.
  Growth slowing due to physical and economic limits.
Clock Rate:
  Grew rapidly until mid-2000s (~3–4 GHz).
  Now mostly stagnant due to:
    Power dissipation constraints.
    Heat limits and diminishing returns from frequency scaling.
These trends drive every architectural decision, from ISA flexibility to microarchitectural layout, memory hierarchy and interconnect design, ensuring systems remain performant, power-efficient and cost-effective over their multi-year product life cycles.

## Slide 11: Trends in Power and Energy in Integrated Circuits
Factors Affecting Power:
  Capacitance (C): Depends on physical layout and number of transistors.
  Voltage (V): Lower voltage reduces power quadratically.
  Frequency (f): Higher frequency increases power linearly.
Strategies for Reducing Power:
  Lowering supply voltage.
  Clock gating and power gating.
  Using multicore at lower frequencies rather than high-frequency single cores.
  Specialized accelerators (e.g., GPUs, AI chips).

## Slide 12: Trends in Power and Energy
Power Distribution and Heat Removal: Modern chips require extensive power pins and multi-layer power/ground meshes; dissipated power must be actively cooled.
The metrics for power regulation include:
  Peak Power: Must not exceed supply capability,excess draw causes voltage drops leading to malfunction.
  Thermal Design Power (TDP): Sustained power the cooling system must handle; cooling and voltage-frequency throttling protect against overheating.
  Energy per Task: Energy = Power x Time. Comparing energy for a fixed workload (not average power) accurately reflects efficiency and battery/cloud costs.
Dynamic Power & Energy (CMOS):
  Voltage reductions yield quadratic energy savings; frequency scaling trades performance for power.
Historical Trend: Transistor counts and speeds rose faster than voltage could drop hence today’s CPUs consume 10s-100s of watts, pushing air-cooling limits and flattening clock-rate growth.

## Slide 13: Trends in Power and Energy in Integrated Circuits
Factors Affecting Power:
  Capacitance (C): Depends on physical layout and number of transistors.
  Voltage (V): Lower voltage reduces power quadratically.
  Frequency (f): Higher frequency increases power linearly.
Strategies for Reducing Power:
  Lowering supply voltage.
  Clock gating and power gating.
  Using multicore at lower frequencies rather than high-frequency single cores.
  Specialized accelerators (e.g., GPUs, AI chips).

## Slide 14: Trends in Cost
Cost-Performance Balance: In most designs (except supercomputers), reducing cost is as critical as boosting performance.
Learning Curve and Yield:
  Manufacturing costs drop over time as yield improves (fewer defects per wafer).
  Higher yield directly halves per-unit cost.
Volume and Commoditization:
  Doubling production volume ≈ 10% cost reduction due to amortized fixed costs and efficiency gains.
  Commodity markets (DRAM, disks, PCs) drive fierce price competition and thin margins, pushing costs down.
Integrated Circuit Cost Model:
  Cost grows roughly with the square of die area.
Fixed Mask Costs:
  Modern mask sets cost >$1 M; low-volume products may instead use FPGAs or gate arrays to lower upfront costs.
Price vs. Cost vs. Operation:
  Selling price must cover R&D, marketing, facilities and profit-margins are 4-12% for most segments.
  In warehouse-scale systems, operational costs (power, cooling, infrastructure) often exceed purchase amortization, architects must optimize for energy efficiency.